## Slide 1
NPDES General Permits
For Storm Water Discharges
Associated with Construction Activity
March 2015
Notes: <number>

## Slide 2
NPDES General Permits
Effective September 24, 2013
No. GAR100001 – Stand Alone Construction
No. GAR100002 – Infrastructure Construction
No. GAR100003 – Common Development Construction
Current NPDES General Permits are available
on the GAEPD and GSWCC websites:
epd.georgia.gov and gaswcc.georgia.gov
Notes: <number>

## Slide 3: NPDES General Permits
Reading and understanding the Permits are essential to maintaining compliance.
e
Expiration Date – July 31, 2018
Notes: <number>

## Slide 4: Summary of Changes
If the permittee failed to submit a NOI Re-Issuance Notification by deadline (December 24, 2013):
  Failure to comply with this requirement shall constitute a violation of the Georgia Water Control Act for each day until an “initial” NOI – Version 2013 is submitted.
  In addition, the permittee must prepare and submit a new ES&PC Plan in accordance with Part IV of the new permits and pay all applicable fees for a new project in accordance with Part II.D of the permits.
Notes: <number>

## Slide 5: Summary of Changes
Part I – Coverage under the Permits - Definitions:
FINAL STABILIZATION – means “…100% of the soil surface is uniformly covered in permanent vegetation with a density of 70% or greater, or landscaped according to the Plan (uniformly covered with landscaping materials in planned landscaped areas), or equivalent permanent stabilization measures as defined in the Manual (excluding a crop of annual vegetation and seeding of target perennials appropriate for the regions).”
Notes: <number>

## Slide 6: Summary of Changes
Part I – Coverage under the Permits - Definitions:
SUB-CONTRACTOR – means an entity employed or retained by the permittee to conduct any type of construction activity (as defined in this permit) at a construction site.
Sub-contractors must complete the appropriate certification course approved by the Georgia Soil and Water Conservation Commission in accordance with the provisions of O.C.G.A. §12-7-19.
Notes: <number>

## Slide 7: Summary of Changes
Part I – Coverage under the Permits - Defintions:
CERTIFIED PERSONNEL means a person who has successfully completed the appropriate certification course approved by the GSWCC. (O.C.G.A. 12-7-19)
  Level I – Subcontractors retained by a Permittee
  Level IA – E&SC Inspectors retained by a Permittee
  Level IB – Regulatory Enforcement Inspectors
  Level II – Design Professionals and Plan Reviewers
Notes: <number>

## Slide 8: Summary of Changes
Part I – Coverage under the Permits - Eligibility:
  For Infrastructure Construction Projects –
  CONTIGUOUS AREAS OF LAND DISTURBANCES for the purposes of this permit, “include those areas of land disturbances solely separated by drilling and boring activities, water of the State and adjacent State-mandated buffers, roadways and/or railways. In addition, contiguous areas of land disturbances include all areas of land disturbances at a sole roadway intersection and/or junction.”
Notes: <number>

## Slide 9: Summary of Changes
Part I – Coverage under the Permits - Eligibility:
  For Infrastructure Construction Projects –
  Coverage under this permit is not required for infrastructure construction projects that consist solely of “routine maintenance for the original purpose of the facility that is performed to maintain the original line and grade and the hydraulic capacity.”
Notes: <number>

## Slide 10: Summary of Changes
Part I – Coverage under the Permits - Eligibility:
  In order to be eligible for this exemption, the infrastructure maintenance project must comply with the following conditions:
  no mass grading,
  stabilized by the end of each day with temporary or permanent stabilization,
  project duration < 120 calendar days, and
  final stabilization implemented at the end of the maintenance project.
Notes: <number>

## Slide 11: Summary of Changes
Part III – Discharges into, or within One Mile Upstream of and within the Same Watershed as, Any Portion of a Biota Impaired Stream:
If when the Initial Notice of Intent is submitted, the Impaired Stream Segment has been listed for the criteria violated, “Bio F” (Impaired Fish Community) and/or “Bio M” (Impaired Macroinvertebrate Community), within Category 4a, 4b or 5, and the potential cause is either “NP” (nonpoint source) or “UR” (urban runoff), the ES&PC Plan must include at least four (4) of the BMPs listed in Part III.C.2. (a) – (u) of the permits.
Notes: <number>

## Slide 12: 305(b)/303(d) List Documents (Final)
Georgia’s 2012 and subsequent “305(b)/303(d) List Documents (Final)” can be viewed on the GAEPD website, epd.georgia.gov.
GIS Data Sets for biota impaired streams are available on the GAEPD website in ESRI Geodatabase 9.1 format and ESRI Shapefile format.
Criteria violated: “Bio F” (Impaired Fish Community) and/or “Bio M” (Impaired Macroinvertebrate Community).
Potential causes: “NP” (nonpoint source) or “UR” (urban runoff).
Notes: <number>

## Slide 13: Total Maximum Daily Loads (TMDL) Implementation Plans
ES&PC Plan must address any site-specific conditions or requirements included in the TMDL Implementation Plan, if the TMDL Implementation Plan for sediment was finalized at least six months prior to submittal of the Initial Notice of Intent.
List of TMDL Implementation Plans can be viewed on the GAEPD website, epd.georgia.gov.
(Permit Reference: Part III.C.1)
Notes: <number>

## Slide 14: Example - Big Creek
Criteria Violated:
Bio M (Impaired Macroinvertebrate Community)
Potential Cause:
NP (Nonpoint Source)
Category:
4a (Water not supporting its use and a TMDL has been developed)
Notes: <number>

## Slide 15: Example - Big Creek
TMDL for Sediment – February 2004
Estimated Sediment Loading Rates for Existing Conditions:
Drainage Area – 47 sq miles
Sediment Rate – 422 tons/sq mile/yr
Total Load – 19,000 tons/yr
Notes: <number>

## Slide 16: Example - Big Creek
Maximum Sediment Loading Rates that Big Creek can assimilate and achieve water quality standards:
WLA (Point Sources) – 0.16 tons/yr
LA (Nonpoint Sourcs) – 13 tons/sq mile/yr
TMDL – 622 tons/ yr
Notes: <number>

## Slide 17: Example - Big Creek
Estimated Sediment Load for Existing Conditions:
19,000 tons/yr
TMDL for Sediment - 622 tons/yr
% Reduction of Sediment Load - 97%
Notes: <number>

## Slide 18: Example - Big Creek
TMDL Implementation Plan – April 2006
Describes local municipal and county E&SC Programs.
Refers to the Erosion and Sedimentation Act and applicable Rules and Regulations.
Refers to the GSWCC Education and Training Certification requirements.
Notes: <number>

## Slide 19: Total Maximum Daily Loads (TMDL) Implementation Plans
If no site-specific conditions or requirements have been included in the TMDL Implementation Plan for the applicable impaired stream segments:
“NPDES construction activities are considered a significant source of pollution and compliance with the Permits should lead to sediment loading for construction sites at or below applicable targets.”
Notes: <number>

## Slide 20: Terms of Permits
Erosion, Sedimentation and Pollution Control Plan
The ES&PC Plan is Critical
The Plan must be prepared in accordance with Part IV of the Permit and the Plan must be implemented and the Plan must provide for compliance with the Permit.
Notes: <number>

## Slide 21: Summary of Changes
Part IV –ES&PC Plan Contents
Each Plan must include the applicable ES&PC Plan Checklist developed the GSWCC, available on both the GAEPD and GSWCC websites – Revised January 2015.
BMPs identified in Part III.C.2.(a) – (u) of the new Permits have been listed in Appendix 1 of the ES&PC Plan Checklists – Revised January 2015.
The ES&PC Plan Checklist should not be used in lieu of reading and understanding all of the Permit conditions. The Checklist does not address Parts I, II, III, V or VI of the Permits.
(Permit Reference: Part IV.D.1.)
Notes: <number>

## Slide 22: Terms of Permits
Part IV –ES&PC Plan Contents
Delineation of on-site wetlands and all State waters located on and within 200 feet of the construction site.
Delineation of the applicable 25-ft and/or 50-ft buffers adjacent to State waters and any additional buffers required by a Local Issuing Authority.
Delineation of all sampling locations and locations where storm water is discharged to a surface water.
(Permit Reference: Part IV.D.1.)
Notes: <number>

## Slide 23: Terms of Permits
As per the Georgia Erosion and Sedimentation Act and local Erosion and Sedimentation Control Ordinances:
STATE WATERS includes any and all rivers, streams, creeks, branches, lakes, reservoirs, ponds, drainage systems, springs, wells, and other bodies of surface or subsurface water, natural or artificial, lying within or forming a part of the boundaries of the State, which are not entirely confined and retained completely upon the property of a single individual, partnership, or corporation.
Notes: <number>

## Slide 24: Terms of Permits
Buffer Determinations for Tidal Creeks and Saltwater Marshes – Judson H. Turner, EPD Director, April 2014 Memorandum - available on the GAEPD website, epd.georgia.gov.
Methodology for Identification of Intermittent and Perennial Streams and Their Origins, Version 4.11, North Carolina Division of Water Quality (Effective September 2010)
Notes: <number>

## Slide 25: Terms of Permits
If groundwater base flows are present, the stream is perennial or intermittent and will require a buffer.
If the feature is dry, then the stream may be intermittent or ephemeral. If there is no flowing water within 48 hours of a rain event, the drainage feature is most probably ephemeral.
Look for well defined channel and point of “wrested” vegetation – vegetation wrested from the channel for “normal stream flow” or “wave action.”
Notes: <number>

## Slide 26: Terms of Permits
Buffers on State Waters are measured from the point where “vegetation has been wrested by normal stream flow or wave action.”
Wrested Vegetation: movement of water that removes soil, debris and vegetation, creating a clear demarcation between water flow and vegetative growth.
Notes: <number>

## Slide 27: Terms of Permits
Stream Buffer Requirements:
Non-trout (warm water) streams: 25-ft buffer on perennial and intermittent streams.
Trout (cold water) streams: 50-ft buffer on perennial, intermittent and ephemeral streams.
The 25-ft or 50-ft buffer requirements can be applicable to ponds, lakes, and reservoirs.
Notes: <number>

## Slide 28: Summary of Changes
Part IV – Additional Stream Buffer Exemptions
Ephemeral Streams (Excluding Trout Streams)
Bulkheads and Seawalls on Lake Oconee and Lake Sinclair
Maintenance, Repair and/or Upgrade of SWCD Watershed Dams when under the Technical Supervision of the USDA NRCS
Stream Crossing for Utility Lines for any EMC or Public Utility under the Regulatory Jurisdiction of the PSC and/or FERC or any Cable Television System
Right-of-Way Posts, Guy Wires, Anchors, Survey Markers and the Replacement of or Maintenance of Existing Utility Structures under the regulatory jurisdiction of the PSC and/or FERC or roadway projects undertaken by DOT or any municipality or county.
Notes: <number>

## Slide 29: Summary of Changes
Part IV – ES&PC Plan – Design Professional
For STAND ALONE and COMMON DEVELOPMENT construction projects, the design professional who prepared the ES&PC Plan must inspect the installation of the initial sediment storage requirements and perimeter control BMPs within seven (7) days after installation.
For non-linear INFRASTRUCTURE construction projects, the design professional who prepared the ES&PC Plan must inspect the installation of the initial sediment storage requirements and perimeter control BMPs within seven (7) days after installation.
Notes: <number>

## Slide 30: Summary of Changes
Part IV – ES&PC Plan – Design Professional
Alternatively, for LINEAR infrastructure construction projects, the design professional who prepared the ES&PC Plan must inspect the installation of the sediment storage requirements and perimeter control BMPs for the INITIAL PHASED SUB-PART OR SEGMENT of the linear infrastructure project and ALL SEDIMENT BASINS within seven (7) days after installation.
Disturbed acreage of the initial phased sub-part or segment of the LINEAR infrastructure project must be equal to or greater than 10% of total disturbed acreage but not less than one(1) acre.
Notes: <number>

## Slide 31: Summary of Changes
Part IV – ES&PC Plan – Inspections
  Primary Permittees and Tertiary Permittees must measure rainfall once every 24 hours except any non-working Saturday, Sunday and Federal holiday until a NOT is submitted.
Measurement of rainfall may be suspended if all areas of the site have undergone final stabilization or established a crop of annual vegetation and a seeding of target perennials.
Notes: <number>

## Slide 32: Termination of Coverage
Termination of Coverage
FINAL STABILIZATION – means “…100% of the soil surface is uniformly covered in permanent vegetation with a density of 70% or greater, or landscaped according to the Plan (uniformly covered with landscaping materials in planned landscaped areas), or equivalent permanent stabilization measures as defined in the Manual (excluding a crop of annual vegetation and seeding of target perennials appropriate for the regions).”
Notes: <number>

## Slide 33: Summary of Changes
Part VI – Termination of Coverage
The Permittee (Primary, Secondary or Tertiary) may submit a Notice of Termination (NOT) immediately if:
All planned construction activities have been completed and the entire development has undergone final stabilization as defined in the new permits,
All storm water discharges associated with construction activities have ceased, and
The site is in compliance with the Permit.
(Permit Reference: Part VI.A.)
Notes: <number>

## Slide 34: Summary of Changes
Part VI – Termination of Coverage
  For Infrastructure Construction Projects –
The permittee may submit a Notice of Termination (NOT) for each phase of the infrastructure project, not to exceed four (4) phases.
The disturbed acreage for each phase must be equal or greater than 25% of the total disturbed acreage – except for the final phase, the disturbed acreage for the final phase must be equal to or greater than 10% of the total disturbed acreage.
Notes: <number>

## Slide 35: Summary of Changes
Part VI – Termination of Coverage
  For Infrastructure Construction Projects –
Permittees may submit a Notice of Termination (NOT) if coverage under the 2013 NPDES General Permit No. GAR100002 is not required for the Primary Permittee of an existing infrastructure construction project.
Contiguous Areas of Land Disturbances and Routine Maintenance for infrastructure construction projects have been redefined in the 2013 NPDES General Permit No. GAR100002.
Notes: <number>

## Slide 36: Summary of Changes
Part VI – Notice of Termination – Attachments
  Copy of the NOI previously submitted for coverage under the 2013 NPDES General Permits for Construction Activities.
Copies of all sampling reports and/or written justification why sampling was not conducted.
GPS locations of the beginning and end of each phase of a linear infrastructure construction project and if applicable, maps identifying significant landmarks.
Documentation that coverage under the 2013 NPDES General Permit No. GAR100002 is no longer required (e.g., resulting contiguous land disturbances less than one (1) acre or routine maintenance).
Notes: <number>

## Slide 37: Summary of Changes
Part VI – Termination of Coverage
The Primary Permittee of a Common Development may submit a NOT, even if all planned construction activities have not been completed, if and only if:
Construction activities have stopped for at least 90 days,
Final stabilization has been implemented by the Primary Permittee and all Secondary Permittees,
All Secondary Permittees have submitted a NOT, and
The site is in compliance with the Permit.
(Permit Reference: Part VI.A.1.)
Notes: <number>

## Slide 38: Summary of Changes
Part VI – Tertiary Permittee – Common Developments
The Primary Permittee must notify the legal title holders of each remaining lot(s) that these lot Owners or Operators will become Tertiary Permittee(s) – applicable to all lots, including lots that are less than one acre.
TERTIARY PERMITTEE means either the Owner or Operator of a remaining lot(s) within a Common Development where the Primary Permittee and all Secondary Permittees have submitted a NOT in accordance with the Permit (excluding utility companies and contractors working under a Blanket NOI).
Notes: <number>

## Slide 39: Tertiary Permittees
OPTION (1) - The owner may submit a Notice of Intent – Initial Notification for each individual lot as a Tertiary Permittee and a new ES&PC Plan for each individual lot must be prepared and submitted. For each NOI submitted, the Tertiary Permittee must submit a NOT.
OPTION (2) – The owner may submit a single NOI – Initial Notification as a Tertiary Permittee for the entire construction site AND if the owner’s construction site is less than five acres and total land disturbance within each individual lot is less than one acre, the owner may submit a new ES&PC Plan for a typical individual lot and then submit a NOT for each individual lot.
Notes: <number>

## Slide 40: Tertiary Permittees
OPTION (3) - The owner may submit a single Notice of Intent – Initial Notification for the entire construction site and submit a new ES&PC Plan for the entire construction site. The owner may submit the NOI – Initial Notification as either a Primary Permittee or Tertiary Permittee and a single NOT.
Primary Permittees must provide copies of the Plan to all Secondary Permittees.
Primary Permittees are solely responsible for the payment of NPDES General Permit fees for all planned land disturbing activities – including land disturbing activities planned by any Secondary Permittees.
Notes: <number>

## Slide 41: Contact Information
GAEPD Contact – Frank M. Carubba
Telephone: (404) 651-8550
Frank.Carubba@dnr.state.ga.us
Notes: <number>