## Slide 1
Best Management
Practices
and
Current
Trends

## Slide 2: BMP Standards and Specifications for Land Disturbing Activities
New BMPs
Flocculants/Coagulants (Fl-Co)- (Vegetative)
Filter Surface Skimmer (Sk)- (Structural)
Seep Berm (SpB)- (Structural)
Temporary Sediment Trap (Sd4) -(Structural)
Turbidity Curtain (Tc)- (Structural)
Tree Protection (Tr) - (Structural)

## Slide 3: Flocculants/Coagulants (Fl-Co)
Coagulants neutralize the repulsive electrical charges
(typically negative) surrounding particles allowing them
to “stick together” creating clumps or flocs.
Flocculants facilitate the agglomeration or aggregation of the coagulated particles to form larger floccules and acts as a net where it gathers up the smaller coagulated particles making a larger particle. The larger particles will slowly drop to the bottom creating a sludge.

## Slide 4
Mixing Chambers

## Slide 5
Mixing Chambers

## Slide 6: Floating Surface Skimmer (Sk):
  A skimmer drains the water from the top allowing cleaner less turbid water to discharge from the ponding area.
  Emergency spillway is required when using a skimmer.
  Can replace the riser pipe as the principal spillway.
  If a skimmer can not be used a rationale/justification must be given.

## Slide 7: Floating Surface Skimmer (Sk):
Floating Surface Skimmers require the following to be shown on the erosion control plan:
  Pond, trap or basin size, length in feet (top and bottom) width in feet (top and bottom) and depth
  Time to Drain (hrs)
  Skimmer Dimensions (orifice and head size in inches)

## Slide 8: Seep Berm (SpB)
A seep berm is a linear control
device constructed as a diversion
perpendicular to the direction of
the runoff to enhance dissipation
and infiltration of runoff, while
creating multiple sedimentation
chambers with the employment of
intermediate dikes.
To allow the 2 year storm event,
24 hour design storm to seep out
while allowing larger flows to be
diverted to a sediment storage area

## Slide 9: Seep Berm (SpB)
Seep Berm require the following to be shown on the erosion and sediment control plan:
  A. Top of Berm Elevation in feet*
  B. Bottom of Berm Elevation*
  C. Top of Berm Width *
  D. Height of the Berm*
  E. Seep Hole Diameter*
  F. Distance from the top of the berm to the seep to be placed in accordance with the 2yr-24hr storm*
  G. Type of Seep
PVC Metal Other(specify)
  H. Spacing of Seep Along the Berm*
* shown in feet

## Slide 10: Temporary Sediment Trap (Sd4)
  BMP added to provide sediment storage options for smaller sites
  All sd4’s to be cleaned out at 1/3rd full
  Provides three options:
    1. Temporary Sediment Trap
– Overflow
2. Temporary Sediment Trap
– Combination Outlet
3. Temporary Sediment Trap
– Rock Outlet

## Slide 11: Temporary Sediment Trap (Sd4)
1. Temporary Sediment Trap - Overflow (Sd4-A)
  An overflow temporary sediment trap is limited to small areas less than 1 acre,
  The maximum life span of an overflow trap is 6 months.
  Silt fence, straw bale barriers or grass filter strips are used to “polish” the overflow water as it leaves the sediment trap.

## Slide 12: Temporary Sediment Trap (Sd4)
2. Temporary Sediment Trap – Combination outlet (Sd4-B)
  The combination outlet uses straw bales and silt fence to dewater the sediment trap.
  Proper installation and staking of the straw bales, and wire backing on the silt fence are required for the materials to resist 1 foot or more of ponded water.
  The combination straw bale and silt fence outlet is limited to 1 acre total drainage area, and has a life span of less than 1 year.

## Slide 13: Temporary Sediment Trap (Sd4)
3. Temporary Sediment Trap – Rock outlet (Sd4-C)
  The rock outlet relies on filtering through layers of aggregate, rock or riprap material to dewater the sediment trap.
  It is the most sturdy of the sediment trap designs and generally requires less maintenance.
  It can be used for drainage area up to 5 acres and has a life span of 1 year.

## Slide 14: Sd4-C detail

## Slide 15: Turbidity Curtain (Tc)
  A floating or staked barrier installed within the water. (It may also be referred to as a floating boom, silt barrier or silt curtain).
  Not to be used as sediment storage.
  Turbidity Curtain is installed to minimize turbidity and silt migration from work occurring within the water or as a supplement to perimeter control BMPs at the water’s edge.
  Silt or turbidity is confined to the area within the boundary created by the installation, such that suspended particles drop out of the water column over time.

## Slide 16: Turbidity Curtain (Tc)
Floating Turbidity Curtains Tc-F
Staked Turbidity Curtains Tc-S

## Slide 17: Tree Protection (Tr)
Tree Protection (Tr)
  To protect desirable trees from injury during construction activity.
Tree Protection Zones:
1. Measure the diameter of the tree trunk in inches at 4.5 feet from the ground.
This is called the
Diameter Breast
Height or DBH.
2. Multiply this value by 1.5.
This result is the diameter
of the root protection zone
in feet. This is also
considered the critical
rooting distance.

## Slide 18
BMPs are used in series to provide a defense against erosion on land disturbance sites using both vegetative and structural measures
Notes: Hard to beat the statement “If it is green it is clean”. Every single one of these bmps talked about and more can be used in a series to promoted clean water and compliance with the Federal and State laws.