## Slide 1: Lessons From Erosion and Sediment Control Litigation 3/19/15 Michael W. Lord Freeman Mathis & Gary, LLP 100 Galleria Parkway Suite 1600 Atlanta, GA 30339

## Slide 2: Manual for Erosion and Sediment Control in Georgia
6th Edition
GSWCC
Written for 4 Audiences
  Land Disturbers
  Enforcers
  Plan Reviewers
  Design Professionals

## Slide 3: 5th Audience
Plaintiff’s Counsel
Not Drafted for Jury

## Slide 4: Jury Trials
Jurors Know Water Flows Down Hill (Usually)
Jurors Know Little About Construction
Jurors Will Pick Who They Relate To
Juries Relate to Who and What They Know

## Slide 5
Best Management Practices shall be required
for all land disturbing activities
OCGA. § 12-7-6(a)

## Slide 6: BMP STANDARDS and SPECS
Are intended to provide minimum criteria
Not intended to be complete
6-1

## Slide 7: SHALL, WILL, SHOULD and MAY
Shall or Will – Mandatory
Should – Advisory condition, recommended but
not mandatory
May – Permissive, no requirement intended
Ga. SWCC p. 6-1

## Slide 8: PLANNING and PLANS
Preliminary Site Investigations
Preliminary Design
Subsurface Investigation
Final Design
Planning Normally Follows These 4 Steps
Ga. SWCC p. 3-1

## Slide 9: STABLIZE Disturbed Areas Immediately
Permanent structures, temporary or permanent vegetation… or a combination of these measures should be employed as quickly as possible after the land is disturbed
p. 2-4

## Slide 10: Fit the Activity to the Topography and Soils
Detailed planning should be employed to assure … permanent features of the activity conformed to the natural characteristics of the site
p. 2-3
Large graded areas should be located on the most level portion of the site
Steep slopes, erodible soils… should not be utilized without overcoming limitations through sound engineering practices
p. 6-9

## Slide 11
The disturbed area and the duration of exposure to erosion elements should be minimized
Clearing limited to only those areas of the site to be developed at a given time
p. 2-3, 6-9

## Slide 12
THE ESCAPE OF SEDIMENTS FROM THE SITE SHALL BE PREVENTED
PLAN NOTE, Ga. SWCC 6-13

## Slide 13
OCGA 12-7-9 REQUIRES CERTIFICATION STATING PLAN PREPARER OR DESIGNEE VISITED SITE PRE PLAN OR VISIT NOT RQUIRED AS PER RULES
Ga. SWCC p. 3-1

## Slide 14: TYPES OF CLAIMS
NUISANCE
TRESPASS
NEGLIGENCE
PROFESSIONAL NEGLIGENCE
RIPARIAN RIGHTS
STATUTORY VIOLATIONS
EJECTMENT

## Slide 15: DAMAGES
NOMINAL DAMAGES
SPECIAL DAMAGES
COMPENSATORY
REPAIR
PUNITIVE
ATTORNEYS FEES

## Slide 16: Lessons from Appellate Cases

## Slide 17: John H. Smith, Inc. v. Teveit (Ga. App. 1985)
Homeowners brought negligence actions against surveyor and developer, alleging that failure to take appropriate measures to keep debris and silt from being washed away from subdivision and clogging storm drains caused flood damage to homeowners’ property.
Properties were damaged by flooding which occurred during a “brief” rainfall.
Jury verdicts in favor of homeowners and against only developer for actual damage and punitive damages. Developer appealed.

## Slide 18: John H. Smith, Inc. v. Teveit – cont. (Ga. App. 1985)
Held: Evidence was sufficient to show that developer’s negligence was the proximate cause of the flood which damaged the homeowners’ properties, notwithstanding evidence indicating that other events and/or the actions of other parties to this lawsuit may have contributed to the injuries.
  The developer had been advised by Cobb County on several occasions to install sediment controls in the drainage areas of the subdivision, and developer had promised to do so.
  The developer installed no hay bales, silt screens or other sediment control devices necessary to control the mud, silt and other debris which would naturally flow towards the homeowners’ properties as the result of its clearing and developing the heretofore undeveloped property.
  Punitive damages 1.5 times actual damages

## Slide 19: Bruce v. Wallis (Ga. 2001)
Neighbor who raised fish in pond on his property brought nuisance action against landowner who trained, bred, and boarded horses on her property, contending that manure on landowner’s property created noxious and offensive odors and that the manure drained into neighbor’s pond and killed his fish.
Landowner submitted two affidavits:
  (1) From civil engineer opining that the steps landowner had taken to prevent sediment from her property from being washed off onto neighbor’s property were “more than adequate to control and possible silt runoff.”

## Slide 20: Bruce v. Wallis – cont. (Ga. 2001)
  (2) From a small pond businessman with B.S. in wildlife biology and Masters in fisheries opining that because of the drought creating low water levels and large amounts of unoxygenated pond water, the file kill in neighbor’s pond was probably due to the sudden displacement of the unoxygenated water during a heavy rainfall which led to suffocation of the fish. He found no evidence that the fish died because of “nutrient loading.”
Landowner presented uncontroverted evidence that she had alleviated the nuisance
Fayette County Superior Court entered injunction requiring landowner to remove all but three horses from her property. Landowner appealed.
Held: Trial court abused its discretion in entering injunction in light of landowner’s uncontroverted evidence that she had alleviated nuisance.

## Slide 21: Sumitomo Corp. of America v. Deal (Ga. App. 2002)
Landowner and neighbor brought nuisance and trespass action against upstream developer for damage to their property allegedly caused by surface water runoff from developer’s manmade detention pond. The landowner’s property was subject to flooding and erosion every time it rained. The flooding and erosion went on for years.
Jury verdict for landowner and neighbor.
  175,738.98 compensatory damages award to downstream landowner; $250,000.00 punitive damages award
Developer appealed.

## Slide 22: Sumitomo Corp. of America v. Deal - cont. (Ga. App. 2002)
Held: $250,000 punitive damages award to landowner was consistent with due process.
  The jury could have concluded that there were numerous, even hundreds, of instances of damage to the landowner’s property. Therefore, the amount of punitive damages awarded by the jury is consistent with the imposition of civil penalties for numerous violations of either the state or county regulations regarding control of erosions. (See Georgia’s Erosion and Sedimentation Act, O.C.G.A. § 12-7-1, et seq.)

## Slide 23: Simerly v. Pulte Home Corp. Superior Court of Forsyth County – September 2011 Ga. Appeals Affirmed 2013
Homeowners owned property downstream from 2 subdivisions owned by Defendant. Defendant’s VP of land development and the subdivision compliance exec in charge of erosion and sediment controls.
Development of the subdivisions involved clearing and grading and other land disturbance and development activities. The developments decreased the forest and pasture land and cause an increase in the amount of runoff from road, driveways and rooftops. Plaintiffs alleged that Defendants failed to install and maintain appropriate erosion control devices that could have reduced the sediment, dirt, storm water, and other pollutants being discharged downstream and into the streams and ponds located on Plaintiffs’ properties.

## Slide 24: Simerly v. Pulte Home Corp. – cont. Superior Court of Forsyth County – September 2011 Ga. Appeals Affirmed 2013
Plaintiffs gave notice to Defendant of its trespass and nuisance and requested that Defendant immediately remove the sediment from the creeks and ponds on their properties. The requested Defendant restore the creeks and ponds to their pre-damage condition and immediately cease the continuing increased discharge of storm water volumes and sediment onto their properties. Defendant refused to take the remedial action.
Plaintiffs filed suit against Defendant, asserting claims for trespass, nuisance, negligence, negligence per se, violation of riparian rights under O.C.G.A. 44-8-1, Ga. WQCA, Ga. WCA, Ga. ERSCA.
Defendant alleged a pond and bridge on a Third-Party Defendant’s property was in part causing the flooding and pollution.
Jury trial in Forsyth County.

## Slide 25: Simerly v. Pulte Home Corp. – cont. Superior Court of Forsyth County – September 2011 Ga. Appeals Affirmed 2013
Verdict: $2,499,980.00 in damages and attorneys fees.
Defendant deleted emails and removed documents from production.
Appeal affirmed.
“A discharge of storm water runoff from construction activities where management practices have not been properly implemented violates the Sedimentation Control Act”.

## Slide 26
JURY TRIALS

## Slide 27: Coffman v. Bramlett, et al. Superior Court of Cobb County – March 2010
Plaintiffs owned 27 acre property in Dallas, Ga. including 20 acre lake used for recreational enjoyment. The Bramlett Defendants purchased property adjacent and upstream to their land for development of a subdivision. A large stream on the land fed into Plaintiffs’ lake. The Bramlett Defendants removed much of the natural vegetation on part of the property and altered the topography, resulting in silt, sediment, storm water runoff and pollution to flow into the stream channel on Plaintiffs’ property and eventually end up deposited in their lake.
Plaintiffs sued the Bramlett Defendants, also naming the contractor for development, the grading company and the plumbing company.

## Slide 28: Coffman v. Bramlett, et al. – cont. Superior Court of Cobb County – March 2010
Plaintiffs alleged Defendants allowed large quantities of silt and sediment to enter the stream and be deposited into their lake, polluting and contaminating it. The also claimed that by increasing the amount and rate of storm water runoff discharged onto their property, Defendants’ actions resulted in threatening the integrity of a nearby dam and downstream property. Further, Defendants violated the Paulding County Code and provisions of the Georgia Erosion and Sedimentation Control Act of 1975, and failed to follow generally accepted development, construction and grading standards. Plaintiffs also alleged Defendants negligently hired and supervised their employees and subcontractors involved in the site work.
Bench trial (Bramlett Defendants failed to appear)
Judgment for Plaintiffs: $743,000.00

## Slide 29: Cochran v. Godfrey Superior Court of Hall County – August 2011
Plaintiffs and Defendant both owned property in Hall County. Defendant conducted certain grading and other land-disturbing activities on their property. The activities caused the redirection of surface waters onto Plaintiffs’ property, resulting in water, sediment, and other material to flow and be discharged onto Plaintiffs’ property. Plaintiffs claimed the sediment and other material from the grading caused damage to their property, including sedimentation and damage to a pond.
Plaintiffs claimed the redirection of waters and sediment onto their property constituted a trespass and nuisance by Defendant.

## Slide 30: Cochran v. Godfrey – cont. Superior Court of Hall County – August 2011
Defendant claimed that his pasture land was zoned agricultural and was used only for agricultural purposes. He maintained that certain activities fell within the agricultural exception for land disturbance regulations under the Erosion and Sedimentation Control Act of 1975, including the preparation of pasture land and livestock management practices. (He had a fence and barn built so that he could better maintain and manage his horses.) Therefore, Defendant alleged that there was no legal requirement that silt fences or other erosion control measures be taken pursuant to the Act. However, out of caution to protect the grading and grass seed, several silt fences were put in place. Despite the precaution, extremely heavy rain and a hurricane hit the property. Therefore, Defendant maintained that he was an “innocent trespasser” because his entry onto Plaintiffs’ land was unintentional and non-negligent.
Jury trial
Verdict: $104,000.00

## Slide 31: Robinson v. Walker Superior Court of Cherokee County – August 2006
Plaintiff owned property next to Defendant in a subdivision. The rear of Plaintiff’s property was adjacent to Defendant’s property. Defendant began redeveloping his property in 2004. He clear cut the trees, stripped the land with heavy equipment and moved a house onto the property. In the process, he constructed an 250 ft. long earthen dam to create a detention pond. The dam was designed to collect storm water runoff and discharge it through a large concrete structure. Plaintiff claimed the runoff was aimed directly onto the middle of her property, resulting in flooding and damage to her property. Plaintiff approached Defendant about the damage to her property, which included flooding, sediment discharge and silt buildup, but he ignored her concerns.
Plaintiff sued Defendant for continuing nuisance and trespass.

## Slide 32: Robinson v. Walker – cont. Superior Court of Cherokee County – August 2006
Plaintiff alleged Defendant showed willful misconduct, malice, fraud, and wantonness and his actions were in bad faith, was stubbornly litigious and caused unnecessary trouble and expense. She alleged Defendant frequently operated his heavy construction machinery, including a bulldozer, at unreasonable times does the day and night, knowing that it disturbed Plaintiff and other neighbors. Plaintiff sought damages for the costs to repair her property, as well as the reduction in value of her property, the loss of rental value of her property and the cost of purchasing sand bags and a silt fence.
Verdict: $83,000.00

## Slide 33: Williams v. Ultima Holdings Superior Court of Fulton County – January 2010
Plaintiffs owned property adjacent, downhill and to the north of a large residential subdivision. Prior to development of the subdivision, the subdivision property was covered by trees and natural vegetation that prevented mud, silt and excess storm water from flowing onto Plaintiffs’ property when it rained. During construction of the subdivision, heavy machinery was used to remove all of the natural vegetation and to alter the property’s topography in order to include paved surfaces, residential homes and barren earth. This cased the natural surface water run-off to be artificially increased from the subdivision site onto Plaintiffs’ property. As a result, excess storm water was discharged from the subdivision and accumulated onto Plaintiffs’ property, causing flooding and erosion.
Plaintiffs sued Defendants (the developers of the subdivision), claiming they knowingly and intentionally diverted excess storm water, containing silt and other debris, onto their property, which constituted a trespass under O.C.G.A. 51-9-1, as did the erosion of sediment from the development onto Plaintiffs’ property. Plaintiffs’ sought injunctions, general and special damages, punitive damages and attorney’s fees and expenses of litigation.

## Slide 34: Williams v. Ultima Holdings – cont. Superior Court of Fulton County – January 2010
In the consolidated pre-trial order, Plaintiffs claimed the run-off that had flowed onto their property as “sheet flow” had become directed across it in a “concentrated flow” that was discharged from the pond. The pond diminished the value of Plaintiffs’ property.
Defendants contended that to accommodate storm water, a detention/retention pond and an “SD3” pond were built in compliance with government regulations to prevent rain water and silt from running onto neighboring properties. In addition, the developer installed other erosion control measures.

## Slide 35: Williams v. Ultima Holdings – cont. Superior Court of Fulton County – January 2010
Hurricanes Cindy and Dennis caused record rains in Atlanta around the time Plaintiffs’ reportedly complained to Defendants about flooding on their property.
Fulton County officials met with Plaintiffs and Defendants over run-off concerns, and after examining the ponds, the officials issued no citations. In addition, the company Defendants fired to monitor and control erosion at the site found no flaws that would cause excess water or sediment to flow onto Plaintiffs’ land.
Jury trial
Verdict: $25,000.00

## Slide 36: Camp v. Kennedy Dev. Co. Inc., et al. Superior Court of Gwinnett County – August 2013
Plaintiffs owned residential property in Snellville that had a small natural creek on one side of the property. No problem 30+ years. 1 purchased a 48-acre parcel upstream from Plaintiffs which consisted of natural pasture with trees with the intent to develop a subdivision with 185 lots. Defendant 2 purchased lots from Defendant 2 and was responsible for maintaining BMPs during construction. Development of the subdivision included clearing trees, grading lots, installing utilities, paving roads and a storm water system. Defendant 1’s property did not have detention pond facilities for storm water run-off but obtained rights to enlarge a neighboring HOA’s pond to hold the storm water run-off for both subdivisions. After Defendant 1 clear, Plaintiffs noticed an increase in storm water run-off, the creek overflowed and washed away natural banks. Defendant 1 raised the spillway in an attempt to solve the problem, but Plaintiffs allege it made the problem worse. Plaintiffs alleged the water caused the creek’s banks to collapse and erode away their yard and destroyed. They alleged Defendant 2’s failure to follow best management practices contributed to the excess storm water run-off.

## Slide 37: Camp v. Kennedy Dev. Co. Inc., et al. cont. Superior Court of Gwinnett County – August 2013
Plaintiffs and other residents made numerous complaints to Defendants 1 and 2 and to the City of Snellville. The city issued citations and gave written notices to Defendants 1 and 2, ordering them to make repairs. Defendants 1 and 2 failed to make the necessary corrections ordered by the city.
Plaintiffs sued Defendants 1 and 2 for nuisance and trespass, and alleged Defendants 1 and 2’s failure to follow best management practices, including not maintaining a proper erosion control plan and not protecting the buffer areas along the state creek were violations of EPD requirements, GA common law, and city and county ordinances. Plaintiffs also alleged Defendants failed to meet building industry standards within GA.

## Slide 38: Camp v. Kennedy Dev. Co. Inc., et al., cont. Superior Court of Gwinnett County – August 2013
Jury trial
Verdict: $0
Jury found Plaintiffs 50% at fault and Defendant 1 50% at fault. (Defendant 2 was dismissed by consent following the close of all evidence.)

## Slide 39: Pulte Home Corp. v. Simerly (Ga. App. 2013)
Homeowners brought action against home builder for trespass, nuisance, negligence, negligence per se, riparian rights, unjust enrichment, and ejectment based on builder’s actions in causing excess storm water to enter homeowners’ properties, and builder filed third-party complaints against other property owners, alleging a bridge on their property was the cause of the damage.
Home builder purchased property to develop single family residences. Shortly after starting mass grading and other land disturbing activities, excessive amounts of storm water, dirt, sediment, and development debris were discharged into a creek and ultimately into the ponds located on the homeowners’ properties. Investigations revealed this was caused by builder’s activities upstream and its failure to install and maintain erosion control devices required by law.
Homeowners alleged builder violated its duty under the Georgia Water Quality Control Act, the Georgia Waste Control Act, the Georgia Erosion and Sedimentation Control Act, and regulations issued under these statutes when it failed to abide by a permit issued by the State to discharge storm water.

## Slide 40: Pulte Home Corp. v. Simerly – cont. (Ga. App. 2013)
Home builder engaged in spoliation by deleting emails relevant to the litigation, even after the trial court’s order enjoining builder from engaging in further destruction of evidence.
Jury verdict for homeowners for $2.49 million in damages and attorneys fees.
Builder appealed.
Affirmed.
“A discharge of storm-water runoff from construction activities where best management practices have not been property implemented violates the Sedimentation Control Act.”

## Slide 41: Who Are your Neighbors
THREE CASES SETTLED
Down stream former attorney with time on his hands
Single mom with 2 kids in idyllic setting. Then the rains of 2009
Fish pond 2 blocks from State Hwy. project

## Slide 42: LESSONS LEARNED
PLAN REVIEWER APPROVAL DOES NOT BAR CLAIMS
VISIT THE SITE
DOCUMENT AND RETAIN
PHOTOGRAPH
BE PRO ACTIVE AND RESPONSIVE
BE ABLE TO EXPLAIN THE EROSION CONTROL DESIGN PROCESS
MAINTAIN, MAINTAIN, MAINTAIN