## Slide 1: The Surface Skimmer and other BMPs used to improve the quality of storm water discharged from sediment ponds and basins

## Slide 2: Overview
Introduction
Background
The surface skimmer
Installation and maintenance
Additional BMPs
Summary

## Slide 3: 1. Introduction
It does not matter -
Sediment pond or basin
Temporary or permanent
Large or small
An outlet structure that dewaters from the surface IS REQUIRED

## Slide 4: Reference: GAR100001 Stand Alone pg. 21/35 GAR100002 Infrastructure pg. 21/36 GAR100003 Common Development pg. 24/42
Part IV.D.3.a.3 Erosion, Sediment controls
When discharging from sediment basins and impoundments, permittees are required to utilize outlet structures that withdraw water from the surface unless infeasible. If outlet structures that withdraw water from the surface are not feasible, a written justification explaining this decision must be included in the plan. Outlet structures that withdraw water from the surface are temporary BMP’s and must be removed prior to submitting a Notice of Termination. For construction activities where a NOI was submitted prior to January 1st, 2014, this requirement of the permit is not applicable.

## Slide 5: 2. Background
What happens when new water enters into a pond?
Existing water is displaced
Settling of larger particles occurs, smaller particles remain in suspension for extended time

## Slide 6: And
The entry of new water into ponds creates circulation patterns that result in ‘mix’ with pre-existing sediment.
Unless discharge is controlled, this ‘mix’ will be result in a high turbidity being discharged from the pond, sometimes higher than the turbidity of the inflow.

## Slide 7: The Perforated Riser Pipe

## Slide 8: This is a perforated riser pipe

## Slide 9: What is the quality the water when it enters into a perforated riser pipe?

## Slide 10: Regardless of the elevation, the dirty water at lower elevations leaves at a higher concentration than the clearer water above it

## Slide 11: 3. The Surface Skimmer

## Slide 12: This is a surface skimmer

## Slide 13: Regardless of the elevation, it removes only the water from the top

## Slide 14: Testing and evaluation of the surface skimmer
Testing and evaluation of several skimmers has focused on discharge rates (gpm)
Results of studies of water quality (turbidity) have not yet been published.

## Slide 15: 4. Installation and maintenance
Layout configuration
Access for maintenance is necessary
Flow control
Allows complete control
Removal
Removal is required after the site is stabilized, as the surface skimmer is a temporary BMP.

## Slide 16: 5. Additional BMPs to improve discharged water quality
Pond inlet baffles – reduce the flow energy

## Slide 17: 5. Additional BMPs
Baffles – The purpose of a baffle is to retard the flow, and promote sedimentation before the particles reach the riser.
Stone baffles such as this one should extend from side to side, mid-way between the inflow point and the riser.

## Slide 18: 5. Additional BMPs
Shoreline Protection –reduces erosion at the water-slope interface.

## Slide 19: 5. Additional BMPs
Polymers – provide protection of exposed soil in the pond and
pretreatment to encourage sedimentation

## Slide 20: 6. Summary
Surface skimmers are very effective if installed correctly and augmented with other BMPs
Depending on the make and model, skimmers have differing discharge characteristics
Installation will determine the ease of maintenance

## Slide 21: 8. Summary
Skimmers are an important improvement over perforated riser pipes
Control of the discharge can be absolute, by installing a shut-off valve
The discharge quality of water from a sediment basin or pond can be improved by installing additional BMPs

## Slide 22
Thank You
James W. Spotts