## Slide 1: Erosion Control Day
Let’s Talk Floc:
Using aPAM to Manage Erosion, Sediment, and Stormwater Quality During Construction
Brian M. Free
CPESC, CPSWQ, QSD, CPAg
April 8, 2025

## Slide 2: Overview
Georgia Rules and Regulations – Construction & Solar Development
Anionic Polyacrylamide (aPAM) – introduction
Polymer Enhanced BMPs – improving performance of traditional BMPs
Applications for:
  Erosion / Dust Control
  Sediment Control
  Demucking / Mud Thickening
  Water Clarification / Flocculation
Fundamentals for Effective Flocculation with aPAM
Case Studies
Q&A

## Slide 4
Photos: Georgia DNR, EPD Rural Development Council Presentation 10-24-2022

## Slide 5: GSWCC: MANUAL FOR EROSION AND SEDIMENT CONTROL IN GEORGIA (IMPORTANT NOTES FROM SECTION 6-57)
CRITERIA
Application rates shall conform to manufacturer’s
guidelines for application.
Only anionic forms of Fl-Co shall
be used.
Following are examples of Fl-Co applications within construction storm water ditches or drainageways that feed into sediment basins or other BMPs:
•Fl-Co Bags or Socs that are installed directly in a ditch, pipe or culvert.
•Fl-Co treated ditch checks (i.e. fiber rolls, wattles, or compost logs inoculated or used in conjunction with Fl-Co ).
•Granulated Fl-Co treated rock ditch checks
•Ditch checks with attached Fl-Co Bags or Socs.
•Addition of granular Fl-Co directly into a ditch.
•Erosion control blankets and turf reinforcement mats that
have been inoculated with a Fl-Co .
•“Pump and Treat” systems that use mechanical mixing with
a chemical treatment of a Fl-Co.
Planning Considerations
Since settling of flocculated soil particles requires very slow
moving (still) water, chemical additives should never be
introduced into an outfall BMP where water leaves the
property or enters state waters. In all cases where chemical
additives are used to reduce turbidity, it is essential to
include a sediment basin or sediment trap unless using a
“pump and treat” treatment system.

## Slide 6: aPAM (Anionic Polyacrylamide)
Approved Use Under US EPA Construction General Permit
Extremely Low Toxicity
Anionic PAM (negative charge) safe for fish/aquatic organisms
ANSI/NSF/CAN Certification: Standard 60 Drinking water treatment chemicals
Used for Soil Stabilization, water clarification and mud thickening
6

## Slide 7: Anionic Polyacrylamide (aPAM)
Long, linear, negatively charged polymer chain
Water soluble, granular unwinds into long chain in water
Numerous charge points along polymer chain
Binds small particles creating a large
particle or “floc”
Large flocs can then settle or be captured by other BMPs

## Slide 8
Passive Treatment Technologies W
CASQA 2024

## Slide 9: PAM Formulations
Powder/ Granular
  Erosion Control,
Dust Control
& Water Clarification
Flocculant Log
  Water Clarification
Liquid Emulsion
  Dust & Erosion Control

## Slide 10: Construction Applications
Standard BMPs Ineffective At Controlling Turbidity (Especially In Silt & Clay Soils)

## Slide 11: Polymer Enhanced Rock Checks/Wattles
Polymer Enhanced Rock Check Dams

## Slide 12: Polymer Enhanced Inlet Protection

## Slide 13: Sediment Retention Barrier (SRB)

## Slide 14: SEDIMENT RETENTION BARRIERS (SRBS)

## Slide 15: SEDIMENT RETENTION BARRIERS (SRBS)

## Slide 16: Polymer-Soil Matrix
Polymer + Soil agglomerations attach to each other
This allows soil stabilization and capture within natural fiber mattings

## Slide 17
UCF Stormwater Academy: Rain simulator testing on slope protection BMPs
Raw Slope
PAM Treated
Slope
Discharge
Soft Armoring vs.
Bare Soil

## Slide 18
8 inch / 24 hr. rain event
PAM treated slope
Raw slope

## Slide 20: Soft Armor Technique
Slope Erosion From Road Runoff
Regrade Slope, Install Jute Matting, Turf Grass Seed, Apply PAM Blend

## Slide 21: Erosion and Sediment Control
PAM holds seed, soil, fertilizer in place during vegetation establishment
PAM adds >500% more moisture holding ability to soil
Grass germinates quickly
Fast, easy installation

## Slide 22: Dosage: Soil stabilization
10-50 pounds aPAM per acre (12-56 kg/HA)
Soil type
  Site specific pam
  General characteristics for dosing
Slope
o dosing
Rainfall (frequency/ duration)
  Lifespan/ reapplication

## Slide 24: Dust Control
Responsible For Keeping Dust Down and Soil on Site
Drought and High Temperatures
Wind Erosion
Haul Roads, Stockpiles, Tailings
Can Be Difficult in High-Traffic Areas
Lifespan
  Weeks To Months

## Slide 25
Dust Control
PAM material is designed to agglomerate very fine particles while still allowing water to penetrate the soil.
Reduces fugitive dust from haul roads, waste dumps, tailing piles, and open areas on construction sites.

## Slide 26: Anionic Polyacrylamide -Liquid Emulsion- Erosion Control & Dust Suppression
Application Rate:
1 gallon emulsion : 1000 gallons of water
3000 gallons mixture per acre
Add Emulsion To Water
One Application of Dust Stop
Water Only Afterwards
26

## Slide 27: Soil Thickening With aPAM During Sink Hole Repair

## Slide 30: aPAM Flocculant Applications for Water Clarification
Soil Specific Polymer
(must be tested before
application)
SOIL
POLYMER
Polymer + Soil Matrix Forms an Agglomeration

## Slide 31: Why Chemical Additions?
Many common pollutants are not removed by conventional erosion, sediment or stormwater BMPs
Common Pollutants
  Colloidal clays and silt
  Metals
  Nutrients
  Bacteria
Solution?
  Flocculants (anionic PAM)

## Slide 32
The 5 Fundamentals For Effective Flocculation
1. Formulation
2. Dosage
3. Reaction Time
4. Mixing
5. Floc Capture

## Slide 33: Sampling & Analysis
https://www.youtube.com/watch?v=JJDf24A0sOw

## Slide 34: Performance (Jar) Testing
Selection Of PAM Formulation Is Based On Site Specific Analysis
Testing Identifies the Effective Formulation(s)
One PAM Does Not Work On All Soil and Water Chemistries
Sample Analysis Informs
  Most Effective Formulation
  Reaction Time
  Size Of Floc (Settling Speed)
  Expected Clarity (NTU- Initial And Final)

## Slide 35: SOLAR FARM SAMPLES
Performance testing polymers with soil and water samples helps to ensure full reactivity of the Treatment Chemicals and reduces the potential for excess (unreacted) product to discharge from the site.

## Slide 36: Dewatering Ditch System Passive/Semi-Active Treatment
Floc Logs
Mixing/Dosing/Reaction time
Particle Capture
36

## Slide 37: Flocculant Installation
Flocculant Placement:
Flocculants should be installed within flow path
Placed in upper 1/2 to 1/3 of channel
Place in areas of turbulent flow

## Slide 40: Particle Capture = Clear Discharge

## Slide 41: Particle Curtains Placed After Treatment Zone

## Slide 42: Sediment / Settling Basins
42

## Slide 43: Sediment Removal (Demucking)

## Slide 45
aPAM Allows Recycling of Muck as a Topsoil Amendment

## Slide 46: Passive Treatment Applications
CASQA 2024
Open Channel
Pump & Pipe
Tanks
Drain Mixing Grids s

## Slide 47: Open Channels

## Slide 48: Open Channels – Split Pipe

## Slide 49: Plastic Lined Ditch Treatment System

## Slide 50: Treatment Train with Fiber Roll Check Dams and aPAM

## Slide 51: In-Pipe Treatment System
Semi-Passive Treatment System
  Requires Energy
CLOSED - Recirculation
OPEN – Pump and Release
Inexpensive
Portable
Easy Set Up And Take Down

## Slide 52: Pump & Pipe

## Slide 53: Pump & Pipe

## Slide 54: Pump & Pipe

## Slide 55: Closed Pipe Treatment

## Slide 56: Drains

## Slide 57: Drains

## Slide 58: Tanks

## Slide 59: Tanks

## Slide 60: Tanks

## Slide 61: Maintenance and Troubleshooting
Maintenance
PAM dissolves!
  Replace when fully dissolved or mostly dissolved
Ensure Floc Logs are clear of sediment and debris
Maintain other ESC BMPs as directed
Clear out particle capture devices

## Slide 62: Mai
ntenance
and Troubleshooting
Troubleshooting
• Check the 5 Fundamentals first!
• Do you see floc formation?
• Are logs or other BMPs covered and/ or full of sediment?
Floc Logs
Mixing System
Particle Capture

## Slide 63: Training and Troubleshooting Examples:

## Slide 64: Gas Pipeline Project
Mixing Ditch with Particle Capture

## Slide 65: Field Jar Testing To Confirm Polymer Blend
Add PAM Blend & Mix (30, 45, 60 seconds, Record)
Select Best PAM Blend (Record)
Raw Sample (Label, Measure Turbidity, Record) Partition Jar Test Samples (Label, Record)

## Slide 66
Look For Floc Formation

## Slide 67
Built/operated hundreds of PAM treatment
systems.
Extremely successful at water treatment.
Near drinking water quality discharges.
Easy to remotely troubleshoot after site training.
Highly skilled at using polymers in extreme and remote locations.

## Slide 68: Clover Bar Ravine – Edmonton, Canada
Stream Restoration
Metal and TSS contamination
Aggregate Mining & Processing Effluent
Fish bearing stream needed environmentally friendly solution

## Slide 69
Aggregate wash water was discharging directly to a fish bearing stream.
Fish species in the Northern Saskatchewan River:
Burbot
Goldeye
Lake Sturgeon
Mountain Whitefish
Northern Pike
Sauger
Sucker
Walleye
69

## Slide 70: Treatment Train Design:
Capture metal bound particulate
Fit within stream channel footprint
No pumps or tanks for chemical dosing
System must survive winter with minimal maintenance in spring
Materials used in the stream must be non-toxic to aquatic life

## Slide 71: Clover Bar Ravine
Polymer Enhanced Passive Treatment System:
Soft armoring along stream channel and downstream area (jute lined)
Granular PAM applied to assist particle capture system
Duplex FLOC LOG treatment of stream water (703d#3 & 706b)- to reduce metals & turbidity

## Slide 72: Soft Armoring Applied In Stream Channel And Along Embankment
Treatment In Place For Three Years
Before and After Metal and TSS Analysis
Removal Efficiency Varied by Metal
47-95% Removal Range
Average Decrease = 78%

## Slide 73: Polymer Logs Installed In Duplex At 3-m Intervals

## Slide 74: Particulate containing metals captured on jute. Clear water discharge downstream.

## Slide 76
 | 2007 | 2008 | 2010
Metal | % Removal | % Removal | % Removal
Al | -47.7 | -92.1 | -89.7
Cu | -81.8 | -68.2 | -50.0
Fe | -70.0 | -90.6 | -90.4
Pb | -66.7 | -93.0 | -90.3
Ni | -70.0 | -56.7 | -84.5
Zn | -88.3 | -74.5 | -85.1
TSS | -79.0 | -88.4 | -95.8

## Slide 77: pH Log
Insert picture
77
Used In Flowing Water
Ph Decreased 1-2 Units (Slightly Acidic)
Safe To Handle, Food-grade Polymer
Replaces Dangerous & Bulky Chemical Feed Systems

## Slide 78: Rapid Water Clarification: Pond Clear+
No mixing required

## Slide 79: Effective Treatment Results
Turbid canal before Pond Clear treatment
Canal 24 hours after Pond Clear treatment

## Slide 80: Thank you!
Brian M. Free CPESC, CPSWQ, QSD, CPAg
bfree@APSfloc.com
mobile: 336-458-6211